## Slide 1: Basic Principles of Hysteroscopy
Atefeh Gorgin.MD
Fellowship of advanced laparoscopy & Endometriosis

## Slide 2
Hysteroscopy is a safe & high efficient procedure
Proper hysteroscopic evaluation requires:
-Perfect knowledge of the technique
-Accurate patient screening
Without any sedation or anesthesia, while keeping patient discomfort to a minimum.

## Slide 3: Office Hysteroscopy
Outparient, not in operative theather.
No interest:
-Premedication
-Misoprostol
Painless if:
-Salin than carbon dioxide
-Small hysteroscope (3mm) than bigger one
-Vaginoscopy than traditional approach

## Slide 4: Technique of Diagnostic or Office Hysteroscopy
Use of reduced-caliber
Oval-shaped instruments
Not necessary to dilate the cervical canal neither anesthesia nor sedation
For distension 0.9% physiological saline solution is used for diagnostic and surgical vaginal hysteroscopy, only bipolar (not the unipolar!) technique be used
Favorable time : first half of the menstrual cycle, 6-9Th days

## Slide 5
DOING:
Passage of isthmus is a true point
Panoramic view of to systematic evaluation of possible lesion
Base of uterus, rt ostium, lt ostium, Ant wall, Post wall, cervical channel
Base of uterus
Rt ostium
Lt ostium
Post wall
Cervical channel
Ant wall

## Slide 6
Medical history
Explanation of the techniques
Gynecological position
Informed consent should be obtained
Bimanual examination
Patient Preparation

## Slide 7: Preparation for Office Hysteroscopy and Operating Room Setup
A well-equipped & well-organized operating room
The surgeon must Know the instrument and the equipment’s layout perfectly.
Before procedure:
All instruments
The continuous-flow system
The HF electrosurgical unit
The video system
An assistant or a highly qualified nurse
All members of the surgical staff must be trained
Must be check
TELEPACK X
keyboard
documentation pack
LCD color monitor
a 24-Watt cold light source
camera control unit

## Slide 8: Instrumentation:
The telescope is 2.9mm,30° forward oblique vision,5mm external sheet,two channel
The scope sheath: 0.8–1.4 mm
The instrument: oval diagnostic-operative sheath- diameter of 3.2 x5.3mm(5fr).
Video camera system,cold light source, HAMOU Endomat, HF bipolar electrosurgical unit
Suction:
-Is not routinely used since makes initial entry for diagnosis more difficult
-Is necessary, when there is major bleeding, incompetent cervix, performing office surgery with continuous flow irrigation

## Slide 9
Ideal distension system electronic pump (HAMOU Endomat), allows constant control of intrauterine pressure in millimeters of mercury and of the flow rate
Ideal intrauterine pressure is 100 mmHg, in keeping the pressure similar to average arterial pressure, intravasation of liquid through the arteries dissected during surgical maneuvers is reduced.

## Slide 10
The HAMOU II 4-mm micro-hysteroscope with its examination sheath of 5 mm diameter provides a panoramic view of the entire uterine cavity
The TROPHYscope – CAMPO compact hysteroscope has a thin outer diameter of 2.9 mm and can be loaded either with a diagnostic sheath or a 4.4-mm operating sheath.
The TROPHYscope may be used without sheath for diagnostic hysteroscopy in single-flow mode.

## Slide 11: Indications for hysteroscopy:
Suspicion of the intracavitary lesion
Abnormal Uterine Bleeding
Postmenopausal bleeding
Infertility
Mullerian congenital anomaly
Removal of foreign bodies
Submucosal myoma
Isthmocele
Endometrial polype or thickening
Post partum metrorrhgiae
Permanent contraception

## Slide 12: Contraindicationof Hysteroscopy:
Pelvic Inflamatory Disease (PID)
Acute cervico-vaginitis
Sever metrorrhagia
Pregnancy

## Slide 13: Anesthesia
Hysteroscopic procidures with resectoscope:
Local Anesthesia (epidural-paracervical block)
General Anesthetisia (complicated cases) with orotheracheal intubation.

## Slide 14: Media for Distending the Uterine Cavity:
All hysteroscopic procedures require adequate distension of the uterine cavity:
Media: Gas ( diagnostic) or liquid
Resectoscopy Media:
-High-frequency bipolar intrauterine electrosurgery
-Non-conducting distension medium
Physiologic salin solution is the safest & more appropriate medium.

## Slide 15: Distension Media:
Non-Elecrolyte-Non-Conductive (unipolar current):
  -Solution contain glucose
  -Gycine
  -Dextran(hyskon)-allergy
  -Monitol
  -Monitol-sorbitol
Conductive fluid (bipolar) : Physiologic salin- Ringer
Co2: Elecrtronic hystero-insufflator pressure 100-120 mmHg with flow of 30-60ml/min intrauterine pressurebelow 40-80mmHg to avoid embolism complication

## Slide 16: Complication
Greatest risk of Operation Hysteroscopy:
-Extravasation syndrome
-Distension Medium

## Slide 17: Hysteroscopy in the OR:
Antibiotics: prolonged procedure or requires greater manipulation
IUD : to avoid uterine synechiae - removed after 5-6 weeks
Intra-uterine Foley catheters :
-after myomectomies
- endometrial ablations
-septoplasty
-post-operative bleeding is suspected
Balloon is filled with 3-5 cc
The Foley is removed 15 minutes after being placed

## Slide 18: Cold Light Source:
Cold light source have a major impact on image quality.
A Xenon lamp
A 175-watt light source, for special miniature telescopes ( a 300 watt)
At higher power levels more thermal energy
Fiber-optic or fluid light cables (diameter of 3.5 to 5 mm - length of 180-350 cm)
For standard hysteroscopic procedures, cold light cables with a diameter of 5mm & a length of 180 cm are used.

## Slide 19: Imaging Systems:
Video cameras ‘s quality depends on:
-Resolution (given by number of lines or pixels)
-Sensitivity (Lux)
A high signal-to-noise ratio: Hemorrhages or other reasons for loss of light intensity are reduced to a minimum.
Modern High Definition (HD) cameras offer a very high resolution and almost natural color reproduction
Video recorders and printers / on the market.
Complete systems : such as the AIDA® compact NEO (KARL STORZ Tuttlingen, Germany) /video and audio data to be recorded ,printed and archived

## Slide 20: Endoscope:
Flexible fiberscope: High cost
Rigid rodlens: 0-12-30 degree

## Slide 21: Diagnostic hysterocscopy:
Miniature endoscope: 2.9 mm office hysteroscopy-physiologic saline solution 9%
Micro-hysteroscopy: (2mm telescope) for cervical stenosis
Single-flow operation sheet 4.3 mm inner sheet in the 5mm outer sheet
(BETTOCCHI system) inclue:
-Operating sheeth
-Fiber-optic light connector
-Connector for suction & irrigation tubes

## Slide 22: Operative Hysteroscopes:
Office hysteroscopy : Small endometrial polyps -pedunculated uterine leiomyomas
Telescope
2.9 mm diameter
outer diameter 3.2 & 5.3 mm
Scissors
Essure micro-insert
Biopsy forceps
Various types of probes
Electrodes for unipolar and bipolar coagulation
Operatin instruments
semi-rigid design
diameter of 1.67 mm (5Fr)

## Slide 23: Resectoscopes:
For the resection of abnormal intrauterine tissue- endometrial ablation -septal dissection
Resectoscope
8.7mm(26fr)
7.3mm(22fr)
large uterus (endometrial ablation)
pathologies (myoma) with a diameter larger than 3 cm
myoma is found to have a difficult intramural location
12 ‘angel
Cutting loop
2 sheet:suction-irrigation
Micro-coagulating electrude
22fr & 26fr

## Slide 24
HF electrosurgical unit
Unipolar or bipolar technique.
Tempreture of surrounding tissues:
For distension and irrigation:
-Unipolar surgery: 1.5% glycine solution - sorbitolmannitol
-Bipolar resectoscopy: physiological saline solution
-Bipolar: 40-70 ˚C
-Unipolar: 400 ˚C