## Slide 1: Tips & Trips in Advanced Hysteroscopic Surgeries
Dr Zahra Rezaie
Obsetetrician & Gynecologist & Infertility
Associate Professor

## Slide 2: INTRODUCTION
The skills required to perform advanced hysteroscopic surgery
Tips are provided for success fully inserting device and visualizing the entire uterine cavity
Suggestions as to which setting may suit an individual patient
How to avoid and manage excessive vaginal bleeding

## Slide 3: Insertion of the hysteroscope
Vaginal instrumentation
When dilating cervix, a tenaculum should be placed on anterior cervical lip at 12 o'clock and gentle counter- traction applied to straighten the cervical canal
Distension media delivery
Operative procedures need a continuous flow of fluid, the use of a fluid management system is important
Accurately measuring fluid inflow and outflow is essential for safe practice
A constant intrauterine pressure aids visualization and is key to technical success

## Slide 4: Insertion of the hysteroscope
Intracervical advancement of the hysteroscope
This is the most difficult part of procedure
The key principle is to avoid trauma to the fragile endocervical mucosa can lead to poor views from bleeding and predisposes to false passage formation and uterine perforation
Systematics panoramic inspection of the proximal cervix, using small back-and- forth movements, will usually identify the cervical canal

## Slide 5: Insertion of the hysteroscope
The distension medium open cervix ,creating a microcavity, when not immediately apparent, the operator should consider whether the uterus is acutely anteflexed or retroflexed in relation to cervical axis
Lifting and lowering the hands as the hysteroscope is gently held will angle the hysteroscope more anteriorly or posteriorly, and will usually lead to the identification of the cervical canal and redirection of the objective lens into the axis of the canal. The degree of distal lens angulation needs to be appreciated when manipulating the hysteroscope.

## Slide 6: Tips & Tricks to Traverse the Cervix
The internal cervical os is usually the narrowest portion of the cervical canal
combined with its more fibrous composition, can obstruct entry into the uterine cavity
This means traversing it is the most difficult part of advancing the hysteroscope into the uterine cavity
A slight pause at this point will allow time for the inflowing medium to further distend the uterine isthmus
Optimal alignment between the hysteroscope and axis of the cervical canal is of prime importance

## Slide 7: Tips & Tricks to Traverse the Cervix
Stenosed ‘Pin-point’ External Cervical Os
The recommended techniques to incise the external cervical os
• vaginoscopy using 5 Fr hysteroscopic scissors, graspers or 5 Fr electrodes
• vaginal speculum to visualise the cervix with scalpel point / hand-held pointed scissors / diathermy blade
• vaginal speculum to visualise the cervix with blind cervical os finder / dilators / tapered urethral forceps

## Slide 8: Inspection of the Uterine Cavity
Visualization of both tubal ostia confirms that the uterine cavity has been reached
the hysteroscope should cease at the level of the uterine isthmus
This allows time for the cavity to distend and focal lesions to be identified
start with an initial panoramic view ofthe cavity, obtained with the hysteroscope at the level of the uterine isthmus

## Slide 9: Inspection of the Uterine Cavity
A global inspection allows for a general structural assessment with attention drawn to any focal lesions,such as polyps, fibroids, adhesions or congenital uterine anomalies
The next step is to closely inspect the endometrium by advancing the distal end of the instrument
Slowly withdraw the hysteroscope, again obtaining a panoramic view of the uterine cavity.
it is better inspected in detail on withdrawal, as the canal has been nicely expanded by inflowing distension medium

## Slide 10: Inspection of the Uterine Cavity
The camera must remain fixed in position to maintain orientation and facilitate diagnostic evaluation
Familiarity with manipulating an angled lens and orienting within the uterus is fundamental to resectoscopy and the use of miniature electrodes or mechanical instruments within operative hysteroscopes

## Slide 11: Tips for obtaining a good view at hysteroscopy
Menstrual timing:
the early proliferative phase of the menstrual cycle
However, with modern, continuous-flow hysteroscopes, adequate views may be obtained, except in cases of enlarged uterine cavities or friable endometrial cancers

## Slide 12: Tips for obtaining a good view at hysteroscopy
Focusing the hysteroscope:
This should ideally be done with white balance adjustment prior to commencing the procedure
Ensuring adequate illumination:
A dark view may be obtained with larger uterine cavities or in the presence of bleeding
Poor illumination may also arise from damaged light cables, malfunctioning light boxes, or incompatible connections

## Slide 13: Tips for obtaining a good view at hysteroscopy
Avoiding bleeding or fragmentation of endometrial tissue:
Avoid cervical dilatation and traumatising the cervical or uterine sidewalls
Avoid touching intrauterine abnormalities, such as vascular submucous fibroids or hyperplastic endometrial lesions, until the end of the procedure, if at all
Avoid unduly high distension pressures that may stimulate endometrial bleeding as pressures fluctuate and the tamponade is lost
Use miniature hysteroscopesto reduce inadvertent tissue trauma or the need for cervical dilatation

## Slide 14: Tips for obtaining a good view at hysteroscopy
Ensuring adequate outflow:
tight cervical canals may preclude adequate outflow and hence fluid circulation (inflow and outflow) is suboptimal and collected endometrial debris or blood cannot be cleared
Check the outflow tap on the hysteroscope is open (if a continuous-flow hysteroscope is being used)
Cervical dilatation may be required under these circumstances to create a ‘natural’ outflow in the absence of continuous-flow irrigation

## Slide 15: Hysteroscopic Forceps
the open biopsy forceps are pushed into the target area, closed and withdrawn
often with a simultaneous twisting motion to grasp as much tissue as possible
The sample can be removed down the operating channel but this risks it becoming partially or wholly detached and ‘lost’
A preferable approach is to withdraw the entire hysteroscope from the uterine cavity with the biopsy forceps kept closed